Phone Care,Inc.

20142 Ecorse Rd

Taylor, MI.  48180

PHONE (313) 388-9670

FAX (313) 388-9677

___________________________________________________________________________

DX-80 SYSTEM TIME & DATE

The DX-80 system provides a built-in time clock to track System Time.

The clock is battery protected from power failure.  System Time can be changed at any Digital Speakerphone using the Attendant password.

Conditions;

System Time and Date must be set in Database Administration for

proper display at digital Executive Speakerphones and all other

time-sensitive feature operations.

Default Settings;

Programming;

Note: [back],[next],[show],[chg],[bksp], and [save] are LCD

interactive button operations.  Use the three buttons below

the LCD display to actuate the associated operation.

1. Enter Database Administration using the feature code,

press ([Feature],#,*) then password (########)

Note: Password is Quantity of 8 ‘#’ keys.

press [show]

2. Input 08-14, then press [Save]. This advances to the System Time Programming screen.

*  Press [show], the Year database item displays.

*  System Time – Year ‘99’ (range is 0~99)

Press [chg], to change the year for the system clock.

*  Follow this convention for each of the database items for the system clock.

OR....

*  Press [next] This advances to the next system clock item that requires changes.

System Time – Month ‘JAN’ (range is JAN~DEC)

*  Press [next] This advances to the next system clock item that requires changes.

System Time - Day ‘1’ (range is 1~31)

*  Press [next] This advances to the next system clock item that requires changes.

System Time - Weekday ‘FRI’ (range is SUN~SAT)

*  Press [next] This advances to the next system clock item that requires changes.

System Time - Hour ‘00’ (range is 0~23)

*  Press [next] This advances to the next system clock item that requires changes.

System Time - Minute ‘00’ (range is 0~59)

3. Press [ON/OFF] two times to end System Time programming.

Dx80-_t80.doc rev 031502